## Slide 1
The most significant parts of an authenticator are typically harder to forge or manipulate without detection, providing a more robust defense against security threats such as replay attacks or data tampering.
Truncation to MSBs is also aligned with standard practices in cryptographic protocols.

## Slide 5
The creation of a Secured I-PDU
This Process consists of the following six steps:
  Prepare Secured I-PDU
  Construct Data for Authenticator
  Generate Authenticator
  Construct Secured I-PDU
  Increment Freshness Counter
  Broadcast Secured I-PDU

## Slide 6
Calculated MAC
The data, on which the Authenticator is calculated:
  the Data Identifier of the Secured I-PDU (parameter SecOCDataId)
  Authentic I-PDU data
  the Complete Freshness Value.
  These are concatenated together respectively to make up the bit array that is passed into the authentication algorithm for Authenticator generation/verification.
  Data Id = 16-bit
  DataToAuthenticator = Data Identifier | secured part of the Authentic I-PDU | Complete Freshness Value.
SecuredPDU = SecuredIPDUHeader (optional) | AuthenticIPDU | FreshnessValue (optional) | Authenticator (MAC)

## Slide 7
Depending on the authentication algorithm used to generate the Authenticator, it may be possible to truncate the resulting Authenticator (e.g. MAC) generated by the authentication algorithm.
Truncation may be desired when the message payload is limited in length and does not have sufficient space to include the full Authenticator.
Notes
In case a MAC is used, it is possible to transmit and compare only parts of the MAC.
This is known as MAC truncation.
However, this results in a lower security level at least for forgery of single MACs.
While we propose to always use a key length of at least 128 bits, a MAC truncation can be beneficial.